## Slide 1
Amberg IMS Survey Overview

## Slide 2: Content
  Starting point
  What is IMS Survey?
  Different use cases
  System configurations
  Measurement workflows
  Data processing, analysis and reporting/export
2

## Slide 3: Starting point (1)
  IMS Systems: IMS 1000 / 3000
    Measurement method established in market (especially from VMS systems)
    Highly efficient track surveying
    Still high accuracy reachable
  Limitation today
    Necessity of having design data available during survey and for processing
  Track situation
    Most tracks without actual design data
    Track owner aware of benefits of regular 3D track surveying for Track-LCC
3

## Slide 4: Starting point (2)
Conclusion
    IMS System can not yet be used under all desired project conditions
    Existing track without design data shall be measured and evaluated efficiently
    This fact requires a new application
 IMS Survey
4

## Slide 5: What is IMS Survey?
Characteristics
  Usage of high-performance IMS long-chord principle
  Enabling high performance track survey with subsequent data processing and visualisation, even with no or only reduced design data
  From evaluation of inner track geometry (e.g. versines) up to absolute 3D track geometry
    Different application use cases now available
5

## Slide 6: IMS Survey – Use case 1
  Instant / One-off Inner Track Geometry Assessment
  Determination of inner track geometry of a(n) (unknown) track section
  Visualisation and analysis of inner track geometry with TGR
  Reference stationing might be available (optional)
  Reproducibility only possible with known stationing
A
B
(km)
6

## Slide 7: IMS Survey – Use case 2
Inner Track Geometry Assessment & Monitoring
  As Use Case 1, additionally:
  Use of lasting stationing references
  Base for repeatable measurement campaigns
  Design (= derived from initial survey) vs. As-built (= subsequent survey) comparison
    Versines
    Gauge
    Superelevation
    Twist
A
B
km
km
km
7

## Slide 8: IMS Survey – Use case 3
Local 3D Topographic Survey
  Setup and survey of local track reference points (CPs) during initial measurement run
  Track survey in between CPs in local 3D grid (Origin of local coordinate grid = Start of track)
  Results can be used for
    Local track design & track works
    Monitoring design vs. as-built comparison
  Reduced Coordinate Consistency and Coordinate Grid Quality
CP
(Hor. / vert. offset)
Y
Track
X
8

## Slide 9: IMS Survey – Use case 4
Global 3D Topographic Survey
  As Use Case 3, additionally:
  CPs established in Global Coordinate Grid
  Base for
  a) Subsequent transformation of local 3D track data
  or
  b) Initial survey directly using 3D CP project data
  Consistent Coordinate Grid Quality
  Fully compatible with other geodetic 3D survey data
CP
(E/N/H)
N
E
Track
9

## Slide 10: IMS Survey – Summary of use cases
Use case | Short description
1 | Instant / One-off Inner Track Geometry Assessment
2 | Inner Track Geometry Assessment & Monitoring
3 | Local 3D Track Assessment
4 | Global 3D Track Assessment a) Subsequent transformation with 3D CPs b) Initial survey directly using 3D CPs / GNSS
10

## Slide 11: System configurations (1) IMS 1000 / 3000
IMS 1000
IMS 3000
  GRP System FX
  AMU 1030
  Leica total station (TS15/16/ 30/50/60, MS50/60)
  GNSS Option
  GRP System FX
  AMU 1030
  Amberg Profiler 110 FX
  GNSS Option
11

## Slide 12: System configurations (2) IMS 1000 / 3000 – fixed-point measurement device
IMS 1000 – Tachymeter
  Integrated Leica Tachymeter
    TS15/16/30/50/60 / MS50/60
    ATR, motorised
    Visible laser beam
  Automatic fixed-point measurement
  Fixed-point accuracy
    Prism: +/- 1 mm
    Reflectorless: +/- 1.5 mm
  IMS 3000 – Profiler 110 FX:
  Manual fixed-point measurement
  Fixed-point accuracy +/- 3 mm
  Visible red laser allowing reflectorless measurement
12

## Slide 13: Measurement method (1) IMS 1000 / 3000 – Use cases 1+2
  Speed up to 5 km/h
  Start measuring at known stationing reference (optional)
  Kinematic acquisition of inner track geometry
  Update of stationing references (if available/desired)
  Inner track geometry accuracy: 1 mm for 150 m chord length
KM
127
1
KM
127
2
KM
127
3
KM
127
4
KM
127
5
13

## Slide 14: Measurement method (2) IMS 1000 / 3000 – Use case 3 + 4 b)
  Speed up to 4 km/h
  Start measuring at known 3D CP or newly established CP
  Measure offsets to CPs using P110 / TPS
  Kinematic data acquisition, exception: short stops for CP measurements
  Process track data with 3D CPs or newly established CPs
3D CP
3D CP
3D CP
3D CP
3D CP
3D CP
3D CP
3D CP
3D CP
3D CP
Repeat accuracy [mm] | CP Interval [m]
+/- 1 | < 60 m
+/- 2 | < 120 m
+/- 5 | < 300 m
14

## Slide 15: Measurement method (3) IMS 1000 / 3000 – Use case 4 b)
  Combination of
    High accuracy inner track geometry coming from IMU
    with absolute position from GNSS
  As-built survey in absolute coordinate system without any given design data (alignment/CPs)
  Creation of control points during initial survey
  Simple preparation of future maintenance tasks
  Direct BIM/CAD compatibility
15

## Slide 16: Data processing, analysis and reporting/export
  Simple data flow from measurement computer back into office project thanks to given sub-folder structure
  Merging of independent measurement sequences (from different systems and / or different jobs) into one application for further analysis
  Fully automated data processing
  Data analysis, visualisation, reporting and exporting in existing Amberg Rail track applications
  Support of different export formats like ASCII, DXF, LandXML
  Use of Track Geometry Record (TGR) application for assessments
16

## Slide 17: TGR add-on Analysis – Reporting – Exporting
TGR – Track geometry record
Add-on for extended track geometry analysis
More than 80 track parameter incl.
  Gauge, cross level (cant), twist, curvature, versines, a.o.
  Nominal-actual deviations
  Change of deviations
Graphically presented as configurable measuring trace
Comprehensive reporting incl. scaled diagram plots
Amberg IMS Survey
17

## Slide 18
Amberg Rail 3.0
Railway Surveying for Professionals
www.ambergtechnologies.com
e-mail: rail@amberg.ch / support.rail@amberg.ch
How can we help you?
Please contact Amberg Technologies or our local distribution partner: